## Slide 1
Computer Network
Spring 2020
Prof./Dr. Shen Bichuan
School of Electrical and Electronic Engineering Chongqing University of Technology

## Slide 2: What is this Course All About
Fundamental principles of Computer Networks
First course – Broad coverage of topics (important topics in depth)
Topics categorized to:
  network architectures and technologies
  protocols
  applications
We will not discuss specific implementations: e.g., how to configure the latest cisco routers

## Slide 3: Why Learn about Networking?
Indispensable part of modern society
  Commercial – e-commerce, banking, inventorying, telecommunications, archiving, health
  Social – critical infrastructure, homeland security, policing
  Human interaction/communication – email, chat, videoconferencing, social networking, entertainment

## Slide 4: Why Learn about Networking?
  Appears in every facet of engineering
  Modern trend – Network every (electronic) device (computers, phones, sensors, planes, cars, TVs, appliances, heart monitors, …)
Prolific field to pursue graduate studies
  Many problems remain unsolved
  Research funding is still strong

## Slide 5: Course Logistics
Textbook
“Computer Networks: A Systems Approach”
L. Peterson, and B. Davie, 5th edition.
Additional References
“Computer Networks”
S. Tanenbaum and D. Wetherall,
5th edition,
Course Website
Lectures, Homework, Useful links,
Supplementary material, Announcements

## Slide 6: Where to find me
Office & Hours:
TBD
My Email: shenbc@cqut.edu.cn

## Slide 7: Class Expectations
Class participation
Keep up with reading material
Complete assignments and projects on time
Submit clean, organized, and concise reports
Identify potential project partners early (in one week, if possible)
Brush up prior knowledge (Probability theory, C Programming)
Follow academic integrity code

## Slide 8: Key to Success
Attendance
  Pay attention to lectures and keep extra notes
  Ask questions
Effort
  Do homework on your own. It’s ok to ask others, but make your own effort
  Read extra material on your own. Wealth of information available (library books, online articles, research papers)
Consistency
  Keep up with the class pace

## Slide 9: Grading Scheme
Homework: TBD
Final Exam: TBD
Assignment | Points
Homework & Labs | 40
Project | 20
Final Exam | 40
Total | 100

## Slide 10: Course Objectives
Develop a fundamental understanding of the network design principles and performance metrics
Become familiar with the mechanisms and protocols for reliable data communication via a computer network
Be able to evaluate the performance of various network technologies and protocols
Think as an engineer: Can specify, characterize, and design network, and understand what technologies should be employed to build a network with particular specifications?
Develop interest in performing research in the area of Computer Networks

## Slide 11: Topics to be covered
Network architectures, performance metrics, layering
Medium access control
Internetworking, routing
End-to-end protocols, flow control
Congestion control and resource allocation
Applications
Network security

## Slide 12: Introduction
Chapter 1

## Slide 13: Uses of Computer Networks
Classification based on application domains, areas, and contents etc.
Domains: personal, home, various businesses and industries, education, finance, medical, social, military
Media: wired, wireless, mobile
Contents: text, voice, music, graphic, images, multimedia, hypertext, video (conferencing and streaming)

## Slide 14: Applications Examples
Resource Sharing
  Common Printer
  Backup Systems
VPN (Virtual Private Networks)
  Ending the limitation of geographic disperse working environments.
Client - Server

## Slide 15: Applications
  Information and Data Sharing
    Many web applications, including social and industries
    Online education
    Email
    VoIP
    Video
    Tele-Conferencing
    Desktop Sharing
    Telemedicine
  e-commerce
    Shopping from home

## Slide 16: Applications
Peer-to-Peer Applications
  P2P
  Sharing Music and Videos
  Email, etc.
Applications that involve interaction between
  a person and a remote user
  Person-to-person communication

## Slide 17: Applications
Person – to – Person Communication
  Audio + Video (Wechat, QQ)
  Instant Messaging (Wechat, QQ, Twitter)
  Online Audio and Music (Radio Channels, Ximalaya, QQ Music, Kugou)
  Online Video (Tencent Video, Baidu Video, YouTube)
  Telelearning
  Social Networking:
    Wechat, QQ
    Facebook, Linkedin
    Wiki – Wikipedia
  Home Shopping (Taobao, JD, Suning, Amazon)
  Finances (Online Banking,支付宝, Wechat)
  Online auctions (eBay)

## Slide 18: Applications
Entertainment:
  MP3 and DVD-quality movies
  TV shows – IPTV (IP TeleVision)
  Interactive Live Digital TV
Game Playing
  Multiperson real-time simulation games.
Ubiquitous Computing
  Smart Home Monitoring
RDIF (Radio Frequency Identification)
  Replacing Bar Codes with a smart deivices that my turn the real world inot the Internet of things.

## Slide 19: Mobile Applications
Mobile computers (handheld and laptops)
  Fastest growing segments in computer history.
  Individuals are able to use their mobile devices to:
    Read and send email,
    Tweet,
    Watch Movies,
    Download Music,
    Play Games,
    Serf the Web
Internet connectivity allows for those applications to be easily built
  Wireless Networks (Cars, Boats, and Airplanes can not have wired Connections)
  Cellular Networks
  Wireless hotspots (802.11 Standard).
  Wireless Networking vs. Mobile Wireless Networks

## Slide 20: Mobile Uses
Smart Phones – Integration of Internet with Telephony
  Driving the wireless-mobile applications
  3G & 4G cellular networks provides fast data services
  GPS is a standard feature
  m-commerce (mobile commerce)
  NFC (Near Field Communication) smart phones act as an DFID smartcard and interact with nearby reader for payment.
Sensor Networks
  Notes that Sense/gather data about state of the physical world.
  It is revolutionizing science
Wearable Computers
  Implantable Devices
    Pacemakers, Insulin pumps, …
    Controllable wirelessly

## Slide 21: Functions Need to Achieve
Addressing: finding destination, MAC/NET layer in OSI model
Connecting: establishing connection between source to destination, PHY/MAC/NET
Transmission: from start to finish
Negotiating: protocol
Managing: large system, network function correctly, devices, nodes, links, servers, bandwidth allocation, managed centrally or by multiple entities
Configuring: devices and services
Arbitrating: conflicting access or collision

## Slide 22: Requirements and Challenges
Connectivity, Scale and Scalability, Efficiency, Reliability, Managibility
Usability:
Scalability: extension and expansion, growing rapidly and uncontrollably
Flexibility:
Quality: system metrics and individual QoS across network, many impacted factors

## Slide 23: Requirements and Challenges
Fairness: access and load fairness, schedule and priority
Reliability: failures including bit errors, burst, block or packet errors, node or link cutoff, complicated by limited resources, heterogeneous devices and nodes, software and networks
Complexity
Security and threat: cybersecurity issues and solutions
Coverage: broad and wide

## Slide 24: Network Elements
Nodes: Special purpose devices
Links: Connections between nodes
PC
server
switch
bridge
router
Optical fiber
Coaxial cable
wireless

## Slide 25: Network Design
The task of connecting nodes via links, so that nodes can exchange information, reliably, timely, efficiently, safely, privately, and with low cost.
Need to define the network architecture, protocols, applications, interfaces, policies, usages.
Let’s start with the architecture
        Directly connected networks
        Circuit-switched networks
        Packet-switched Networks

## Slide 26: What Drives Network Design?
Applications
  WWW, email, chat, videoconferencing, e-commerce, audio/video streaming, VOIP, file sharing
Who deploys the network
  Enterprise, government, end-user
Where is the network deployed
  Home, building, company, organization, city, country, international

## Slide 27: How do we Evaluate a Network
Metrics (think again a transportation network)
  How many cars can it service (throughput)?
  How fast can it service them (delay)?
  How reliable can it service them (collisions, losses, outage probabilities, etc)?
  Can it provide any guarantees (QoS)?
  Any other metrics you can think of?

## Slide 28: Directly-Connected Networks
Point-to-point links: Each node is directly connected to all others via a link
Multiple access: All nodes share the same physical medium
point-to-point
multiple access

## Slide 29: Switched Networks
Circuit-Switched
  A dedicated circuit is established across a set of links
  Example: Telephone network
Packet-Switched
  Data is split into blocks called packets or messages.
  Store-and-forward strategy
  Switches: Store and forward packets
terminal/
host
switch

## Slide 30: Circuit-Switched Networks
End-to-end permanent connection
  Dedicated path for communication
  No need for a destination address since a path is already established
Once communication is complete, connection is ended and links are released.

## Slide 31: Advantages of Circuit Switching
Guaranteed bandwidth (Quality of Service)
  Predictable bitrate and delay
  Good for delay-sensitive applications
Reliable communication
  Rare packet loss
  Packets are delivered in order
Simple data routing
  Forwarding based on time slot or frequency (multiplexing)
  No need to inspect a packet header for address
Low per-packet overhead
  Forwarding based on time slot or frequency
  No IP (and TCP/UDP) header on each packet

## Slide 32: Disadvantages of Circuit Switching
Wasted bandwidth
  Bursty traffic leads to idle connection during silent period
Blocked connections
  Connection refused when resources are not sufficient
  Unable to offer “okay” service to everybody
Connection set-up delay
  No communication until the connection is set up
  Unable to avoid extra latency for small data transfers
Network state
  Network nodes must store per-connection information
  Unable to avoid per-connection storage and state

## Slide 33: Packet Switched Networks
Data is divided into packets (messages)
  Each packet contains identification info (source/destination address seq. number, etc)
Packets traverse the network individually
  Use the destination address to forward packets
  May use more than one routes, nodes may store packets temporarily

## Slide 34: Advantages of Packet Switching
No wasted bandwidth (not entirely true)
  Links are not reserved during idle period
Multiplexing (see next slides)
  Frequency, time, statistical multiplexing
Service
  More connections of lesser quality
  No blocking of users
Adaptation
  Can adapt to network congestion and failures

## Slide 35: Multiplexing
Three pairs of senders/receivers share the same physical link to communicate
A switch is multiplexing packets from different senders into one packet stream

## Slide 36: Multiplexing Methods
Time Division Multiplexing
Frequency Division Multiplexing
S1
S2
S3
S1
S2
S3
S1
S2
S3
S1
S2
S3
time
time
frequency
S3
S1
S2
f1
f2
f3

## Slide 37: Multiplexing Methods
Statistical multiplexing
  Division of the communication medium into a number of channels of variable bandwidth

## Slide 38: Disadvantages of Packet Switching
No guaranteed bandwidth
  Harder to build applications requiring QoS
Per packet overhead
  Need a header with source/dest. address, etc.
Complex end-to-end control
  Packets can be lost, corrupted or delivered out-of-order
Delay and Congestion
  No congestion control, can lead to arbitrary delays and packet drops

## Slide 39: Network Hardware (1)
Personal area networks
Local area networks
Metropolitan area networks
Wide area networks
The internet

## Slide 40: Network Hardware
Transmission Technology
Scale

## Slide 41: Network Hardware
Two types of transmission technologies:
  Broadcast
    Communication channel shared by all machines
    Packets send by any machine are received by all the others.
      An address field within each packed specifies the intended recipient.
      If packed is intended for some other machine, it is just ignored
      If packed is indented for the recipient machine then it is processed.
    Wireless network is a common example of a broadcast link
      Communication is shared over a coverage region that depends on the wireless channel and the transmitting machine.
    Broadcast systems usually also allow the possibility of addressing a packet to all destinations.
  Point-to-point
    Connect individual pairs of machines
    Packets (short messages) may have to visit one or more intermediates machines.
    Multiple routes of different lengths are possible.
    Finding good ones is important.
    Unicasting – transmission with exactly one sender and exactly one receiver.

## Slide 42: Network Hardware
Alternative Criteria: Scale
  Distance is important as a classification metric because different technologies are used at different scales.

## Slide 43: Network Hardware (2)
Classification of interconnected processors by scale.

## Slide 44: Personal Area Network
Bluetooth PAN (Personal Area Network) configuration

## Slide 45: Local Area Networks
Wireless and wired LANs. (a) IEEE 802.11 or WiFi.
(b) Switched Ethernet (802.3).

## Slide 46: Local Area Networks (LAN)
Switched Ethernet
  Switch; Hardware that connects two devices point-to-point
  A Switch has multiple ports
Physical vs. Virtual LAN – VLAN
Dynamic vs. Static Channel Allocation
  Static Allocation: Each device is allocated its time slot weather or not it uses it.
  Dynamic methods allow changing the time allocation scheme.
Dynamic Allocation
  Centralized
  Decentralized

## Slide 47: Metropolitan Area Networks
A metropolitan area network based on cable TV.

## Slide 48: Wide Area Networks (1)
WAN that connects three branch offices in Australia

## Slide 49: Wide Area Networks (2)
WAN using a virtual private network.

## Slide 50: Wide Area Networks (3)
WAN using an ISP network.

## Slide 51: Network Software
Protocol hierarchies
Design issues for the layers
Connection-oriented versus connectionless service
Service primitives
Relationship of services to protocols

## Slide 52: Protocol Hierarchies (1)
Layers, protocols, and interfaces.

## Slide 53: Definitions
Protocol – is an agreement between the communicating parties.
Peers – the entities comprising corresponding layers on different machines.
  Peers use the protocol to communicated with each other.
No data is directly transferred from layer n on one machine to layer n on another machine.
  Each Layer passed data and control information to the layer immediately below it until the lowest layer is reached.
  Below layer 1 is the physical medium through which actual communication occurs.
  Virtual communication is shown by dotted lines and physical communication by solid lines the previous figure.

## Slide 54: Definitions
Interface
  It defines which primitive operations and services the lower layer makes available to the upper one.
Network Architecture:
  A set of layers and protocols.
The specification of the network architecture must contain enough information to allow an implementation of the program or the hardware for each layer so that it will obey appropriately the protocol.
Protocol Stack:
  The list of protocols used by a certain system – one protocol per layer.

## Slide 55: Protocol Hierarchies (2)
The philosopher-translator-secretary architecture

## Slide 56: Protocol Hierarchies (3)
Example information flow supporting virtual communication in layer 5.

## Slide 57: Protocol Hierarchies (3)
The peer process abstraction is crucial to all network design.
  Level 4 protocol conceptually think of their communication as being “horizontal”:
    SendToOtherSide
    GetFromOtherSide

## Slide 58: Design Issues
Reliability:
  Network must operate correctly although it is made up of a collection of components that are themselves unreliable.
Error Detection:
  It typically uses codes to locate the erroneously transmitted bit(s) and request re-transmission.
Error Correction
  Correct messages is recovered from the possibly incorrect bit(s) that were originally received.
Routing:
  Finding a working path through a network.
Protocol Layering:
  Networks grow larger over time and new designs emerge that need to connected to the existing networks.

## Slide 59: Design Issues (cont.)
Addressing and Naming:
  Every layer needs a mechanism for identifying the senders and receivers that are involved in a particular message.
Internetworking:
  Different network technologies often have different limitations:
    Not all communication channels preserve the order of messages send on them.
    Differences in the maximum size of a message that the networks can transmit.
Scalable:
  Designs that continue to work well when the network gets large.
Resource Allocation
  Networks work with their resources to provide services to various hosts. If they are not aware of limitations of the networks resources than the network is providing proper resource allocation.
Flow Control
  Feedback from the receiver to the sender is often used to alleviate the problem of the sender swamping the slow receiver with data.

## Slide 60: Design Issues (cont.)
Congestion:
  The problem may occur when the network is oversubscribed because to many computers want to send too much traffic and the network will not be able to deliver them all.
  Overloading problem of the network.
  One strategy is for each computer to reduce its demand.
Quality of Service
  Additional Resources (other then Bandwidth),
  Real-time delivery (for applications that require high throughput),
  Live Video,
Network Security
  How good is the network against different kinds of threats
    Eavesdropping,
    Confidentiality,
    Authentication,
    Integrity, etc.

## Slide 61: Connection-Oriented Versus Connectionless Service
Layers can offer two different types of service to the layers above them:
  Connection-oriented, and
  Connectionless

## Slide 62: Connection-Oriented Service
Modeled after telephone system:
  Pickup-the-phone
  Dial the number
  Talk
  Hang-up
Service User:
  Establishes a connection,
  Uses a connection (sender pushes objects in at one end and the receiver takes them out at the other end).
  In some cases when connection is established, the sender, receiver, and a subnet conduct a negotiation about the parameters to be used:
    Maximum message size,
    Quality of service required,
    Other issues (like …?)

## Slide 63: Connection-Oriented Service
A circuit:
  Another name for a connection with associated resources such as a fixed bandwidth.

## Slide 64: Connectionless Service
Modeled after a postal system:
  Each message carries the full destination address, and
  Each one is routed through the intermediate nodes inside the system independent of all the subsequent messages.
Different Names for Messages:
  Store-and-forward switching: Packet, a message, is processed in full before sending it on the next node.
  Cut-through-switching: when the onward transmission of a message at a node start before it is completely received.
Each kind of the Service can be further characterized by its reliability:
  A reliable service is implemented by having the receiver acknowledge the receipt of each message.
  Acknowledgment service introduces overhead and delays.

## Slide 65: Connection-Oriented Service
Example: File Transfer
  The owner want to be sure that all the bits arrive correctly and in the same order they were sent.
  Almost there are no instances were the consumers prefer service that occasionally scrambles or loses a few bits for the gained speed.

## Slide 66: Connection-Oriented Service
Reliable connection-oriented service:
  Message Sequences, and
  Byte Streams
Message Sequences:
  Message boundaries are preserved.
  Example: Two 1024 byte messages are sent, the arrive as two distinct 1024-byte messages; Never as one 2048-byte message.
Byte Streams:
  Message is send as a stream of bytes with no concepts of message boundaries.
  Example: When a 2048-byte message arrives at the receiver there is no way to tell if they were sent as
    One 2048-byte message,
    Two 1024-byte message, or
    2048 1-byte messages.

## Slide 67: Example of Applications
The transit delays introduced by acknowledgments are unacceptable:
  Digitized voice traffic for Voice-Over-IP (VoIP).
  Digitized video conference
Not all applications require connections. Spam:
  Spammer does not want to go through the trouble of setting up and latter tearing down a connection to a recipient just to send them one more item.
  100% reliability is not essential either.
Datagram:
  Unreliable (not acknowledged) connectionless service.
  It is analogous to telegram service

## Slide 68: Example of Applications
Acknowledged Datagram:
  The convenience of not having to establish a connection, but
  Reliability essential
  Similar to “Return Receipt” for the letter.
  Example: Text Messaging on mobile phones
Request-Reply Service:
  Sender transmits a single datagram containing a request;
  The reply contains the answer.
  Example: Mobile phone sending the query to a “map server” to retrieve the map data.

## Slide 69: Connection-Oriented Versus Connectionless Service
Six different types of service.

## Slide 70: Reliable vs. Unreliable Communication
Why would one prefer unreliable communication vs. reliable one?
  Reliable communication may not be available: Ethernet.
    Packets can be damaged.
    It is up to higher levels of protocol to recover from this problem.
    Many reliable services are built on top of the unreliable service.
  The delays for providing reliable service are not acceptable:
    Real time applications such as multimedia.

## Slide 71: Service Primitives (1)
A service is formally specified by a set of primitives (operations).
Primitives are operations that are available to the user processes to access the service.
The set of primitives available are different for connection-oriented services from those of connectionless service.
Example in the next slide

## Slide 72: Service Primitives (1)
Six service primitives that provide a simple connection-oriented
service

## Slide 73: Service Primitives
The primitives presented in the previous slide might be used for request-reply interaction in a client-server environment:
Server executes LISTEN to indicate that it is prepared to accept incoming connections.
  Blocking system call.
  The server process is blocked until a request for connection appears.
Client process executes CONNECT to establish a connection (1) with the server.
  Specifies who to connect to (parameter giving the server’s address).
  OS sends a packed to the peer asking it to connect (See Figure next slide).
  Client process is suspended until there is a response.

## Slide 74: Service Primitives
The server process can establish the connection by executing ACCEPT primitive (2).
  OS sees that the packet is requesting a connection upon reception of the packet.
  OS checks to see if there is a listener and if so it unblocks it.
  Sends a response back to the client process to accept the connection.
  The arrival of this response then releases the client.
  At this point both client and server a running and they have connection established.
The server will execute RECEIVE to prepare to accept the first request.
  Server does this immediately upon being released from the LISTEN, before acknowledgment can get back to the client.
  The RECEIVE is a blocking call.

## Slide 75: Service Primitives
The client will execute SEND to transmit its request (3) followed by RECEIVE to get the reply.
  The arrival of the request packed at the Server unblocks it so it can handle the request.
  After the server has done the work it will issue a SEND to return the answer to the client (4).
  The arrival of the this packed unblocks the client which can now inspect the answer.
  If further request are required it can make them now.

## Slide 76: Service Primitives
When the client is done it executed DISCONNECT to terminate the connection (5).
  Initial DICONNECT is a blocking call, suspending the client and sending a packet to the server saying that the connection is no longer needed.
  When the server gets the packed it also issues a DISCONNECT of its own, acknowledging the client and releasing the connection (6).
  When the server’s packet gets back to the client machine, the client process is released and the connection is broken.

## Slide 77: Service Primitives (2)
A simple client-server interaction using acknowledged datagrams.

## Slide 78: Service Primitives
Many things can go wrong:
  Timing (e.g., CONNECT is done before LISTEN)
  Packets can get lost, …
Why not using connectionless service:
  Only two (2) packets would be needed vs. six (6), however,
  Large messages
  Transmission errors
  Lost packets
  Etc.
Example:
  How would the client know whether the last packet actually received was really the last packet sent?

## Slide 79: The Relationship of Services to Protocols
A service is a set of primitives (operations) that a layer provides to the layer above it.
  The service defines what operations the layer is prepared to perform on behalf of its users, but it does not say anything at all about how these operation are implemented.
A protocol is a set of rules governing the format and meaning of the packets, or messages that are exchanged by the peer entities within a layer.
  Entities use protocols to implement their service definitions.
  They are free to change their protocols at will, provided they do not change the service visible to their users.
  In this way the service and the protocol are completely decoupled.

## Slide 80: The Relationship of Services to Protocols
The relationship between a service and a protocol.

## Slide 81: The Relationship of Services to Protocols
Key Concept:
  Services relate to interfaces between layers
  Protocols relate to the packets send between peer entities on different machines.
Programming Languages Analogy:
  Service is like an abstract data type or an object in an object-oriented language.
    It defines operations that can be performed on an object bud does not specify how these operations are implemented.
  Protocol relates to the implementation of the service and as such is not visible to the user of the service.

## Slide 82: Reference Models
OSI reference model
TCP/IP reference model
Model used for this text
Comparison of OSI and TCP/IP
Critique of OSI model and protocols
Critique of TCP/IP model

## Slide 83: The OSI Reference Model
Principles for the seven layers
Layers created for different abstractions
Each layer performs well-defined function
Function of layer chosen with definition of international standard protocols in mind
Minimize information flow across interfaces between boundaries
Number of layers optimum

## Slide 84: The OSI Reference Model
The OSI reference model

## Slide 85: OSI Reference Model Layers
Physical layer
Data link layer
Network layer
Transport layer
Session layer
Presentation layer
Application layer

## Slide 86: Physical Layer
Is concerned with transmitting raw bits over a communication channel.
Design Issues:
  Ensuring that when one side sends a 1 – bit of information it is received as 1-bit (not as 0-bit or 2-or more- bits).
  What type of signal should be used to represent “1” and “0”?
  How many nano seconds a bit lasts?
  Whether transmission can occur simultaneously in both direction?
  How initial connection is being established?
  How it is torn down when both sides are finished?
  How many pins the network connector has?
  What each pin is used for? Etc.
Deals with mechanical, electrical, timing interfaces, and the physical transmission medium.

## Slide 87: Data Link Layer
Main task of the data link layer is to transform a raw transmission facility into a line that appears free of undetected transmission errors.
It does this by:
  Break up the input data into data frames.
  Sequential transmission of each frame.
  The receiver confirms correct receipt of each frame by sending back an acknowledgment frame.
  How to keep a fast transmitter from drowning a slow receiver in data.
  Some traffic mechanism may be needed to let the transmitter know when the receiver can accept more data.
  Broadcast networks have an additional issue in the data link layer:
    How to control access to the shared channel?
    A special sublayer of the data link layer, called “Medium Access Control” sublayer, deals with this problem

## Slide 88: Network Layer
This layer controls the operation of the subnet.
Key design issue is determining how packets are routed from source to destination.
  Static tables are wired into the network and are rarely changed, or
  They are changed more often dynamically to avoid failed components.
    They can be determined at the start of each conversation (e.g., login session), or
    They can be highly dynamic and for each packed the new routing can be established depending on the load.
Congestion handling: If two many packets are present in the subnet at the same time, they will get in each other’s way forming bottlenecks.
Quality of Service:
  Delay,
  Transit time,
  Jitter, Etc.
are also a network layer issues.
It is up to the network layer to overcome all the problems that occur in heterogeneous networks so that they may be interconnected.
In broadcast networks the routing problem is simple so the network layer is often thin or even nonexistent.

## Slide 89: Transport Layer
The main function of Transport Layer is to:
  Accept data from above it,
  Split it up into smaller units if needed be,
  Pass these to the network layer,
  Ensure that the pieces all arrive correctly at the other end,
  All this must be done efficiently and in a way that isolated the upper layers from the inevitable changes in the hardware technology over the course of time.
In addition, it is charged for determining what type of service to provide to the session layer, and ultimately, to the user of the network.
Example:
  Error-free point-to-point channel that delivers messages or bytes in the order in which they were send.
  Transporting of isolated messages with no guarantees about the order of delivery,
  Broadcasting of messages to multiple destination.
Transport Layer is a true end-to-end layer; it carries data all the way form the source to the desitnation.

## Slide 90: Session Layer
The session layer allows users on different machines to establish sessions between them.
Services:
  Dialog control - Keeping track the whose turn is it to transmit,
  Token management – Preventing tow parties from attempting the same critical operation simultaneously, and
  Synchronization – Checkpointing long transmissions to allow them to pick up form where they left off in the event of a crash and subsequent recovery.

## Slide 91: Presentation Layer
This layer is concerned with the presentation of the message; that is syntax and semantics of the information transmitted.
It deals with different internal data representations on different machines:
  Abstract data structures,
  Standard encoding to be used,

## Slide 92: Application Layer
This layer commonly contains a variety of protocols that are needed by the users.
For example:
  HTTP – Hyper Text Transfer Protocol,
  FTP - File Transfer Protocol
  POP/SMTP – E-mail Protocol,
  RSS – Network News, etc.

## Slide 93: The TCP/IP Reference Model Layers
Link layer
Internet layer
Transport layer
Application layer

## Slide 94: The TCP/IP Reference Model
Grandparent of all wide area computer networks ARPANET
It’s successor Internet
ARPANET research network sponsored by the DoD.
Used initially leased telephone lines.
When satellite and radio networks were included the new reference architecture was needed.
Hence the ability to connect to multiple networks in a seamless way was one of the major design goals.
This architecture latter became known as the TCP/IP Reference Model.
Design criteria:
  Network be able to survive loss of subnet hardware without existing conversations being broken off.
  Applications with divergent requirements were supported ranging from file transfer to real-time speech transmission.

## Slide 95: The TCP/IP Reference Model (1)
The TCP/IP reference model

## Slide 96: Link Layer
Packet switched network
Connectionless layer that runs across different networks.
The lowest layer, the link layer, describes what links such as serial lines and classic Ethernet must do to meet the needs of this connectionless internet layer.
It is not actual layer in the classical sense of the term rather is an interface between hosts and transmission links.

## Slide 97: Internet Layer
The Internet Layer holds this architecture together.
Its job is to permit hosts to inject packets into any network and have them travel independently to the destination (potentially on a different network).
The packets may arrive in a completely random order from the original and the higher layer must rearrange them – if in-order of delivery is desired.
The internet layer define san official packet format and protocol called IP (Internet Protocol).
Packet routing is a major issue and IP has not proven effective at avoiding congestion.

## Slide 98: Transport Layer
Transport Layer is designed to allow peer entities on the source and destination hosts to carry on a conversation, similarly to the OSI transport layer.
Two end-to-end transport protocols:
  TCP (Transmission Control Protocol) – reliable connection-oriented protocol that allows a byte stream originating on one machine to be delivered without error on any other machine in the internet.
  UDP (User Datagram Protocol) – is unreliable connectionless protocol.

## Slide 99: Transport Layer
  TCP (Transmission Control Protocol) – reliable connection-oriented protocol that allows a byte stream originating on one machine to be delivered without error on any other machine in the internet.
    It segments the incoming byte stream into discrete messages
    Passes each one on to the internet layer.
    At the receiver the TCP process reassembles the received messages.
    Flow control is also managed by TCP to ensure that a fast sender cannot swamp a slow receiver.
  UDP (User Datagram Protocol) – is unreliable connectionless protocol.
    For applications that do not want TCP’s sequencing or flow control and they want to provide one of their own.
    Widely used for one-shot, client-server-type request-reply queries and application in which prompt deliver is more important than accurate delivery.
      Speech
      Video

## Slide 100: The TCP/IP Reference Model (2)
The TCP/IP reference model with some protocols we will study

## Slide 101: Application Layer
Applications must include any session or presentation functions that they require.
Experience with the OSI model has proven this view to be correct: these layers are of little use to most applications.
Application Layer contains all the higher-level protocols.
  TELNET - Virtual Terminal
  FTP – File Transfer Protocol
  SMTP – electronic mail
Many other protocols have been added (see figure in the previous slide):
  DSN – Domain Name System
  HTTP – Hyper Text Transfer Protocol
  RTP – Real-time Transfer Protocol

## Slide 102: The Model Used in this Book
The reference model used in this book.

## Slide 103: The Model Used in this Book
Using the 5 layers:
  Physical
  Link
  Network
  Transport, and
  Application
Value of OSI model is retained for understanding network architecture.
In addition we concentrate primarily on protocols that are important in practice:
  TCP/IP
  802.11
  SONET
  Bluetooth.

## Slide 104: Comparison of the OSI and TCP/IP Reference Models
Concepts central to OSI model
Services
Interfaces
Protocols

## Slide 105: Service
Each layer provides a service to the layer above it.
The service definition tells what the layer does, not how entities above it access it or how the layer works.
It defines the layer’s semantics.

## Slide 106: Interface
A layer’s interface tells the processes above it how to access it.
It specifies what the parameters are and what results to expect.
This layer also says nothing about how the layer works inside.

## Slide 107: Protocol
A layer’s protocol its is own business: it can use any protocols it wants to as long as it gets the job done (i.e. provides the offered services).
A layer is allowed to change the protocol with the condition that it will not affect the software in higher layers.

## Slide 108: Object Oriented Programming
Those ideas fit very nicely with modern ideas about object-oriented programming.
An object has:
  A set of methods (operations) that processes outside the object can invoke.
  A set of data (method’s parameters) that defines the object.
  The code internal to the object is its protocol and is not visible or of any of concern outside the object.
  The object provides the set of services through object’s interface.

## Slide 109: The Properties
TCP/IP model did not originally distinguish between:
  Services
  Interfaces, and
  Protocols
The model was retrofitted after the fact to make it more OSI-like.
However, OSI model has a better hidden then in the TCP/IP model and can be replaced relatively easily as the technology changes.

## Slide 110: The Properties
The OSI reference model was devised before the corresponding protocols were invented.
  This ordering meant that the model was not biased toward one particular set of protocols: a fact that made it quite general.
  The downside of this ordering was that the designers did not have much experience with the subject and did not have a good idea of which functionality to put in which layer.
With TCP/IP the reverse was true: The protocols came first, and the model was really just a description of the existing protocols.
  There was no problem with protocols fitting the model.
  The trouble was that the model did not fit any other protocol stacks: It was not especially useful for describing other non-TCP/IP networks.

## Slide 111: Critique of the TCP/IP Model
Does not distinguish clearly the concepts of services, interfaces, and protocols.
Good Software Engineering practice requires differentiating between the specification and the implementation.
The link layer is really not a layer at all: It is an interface between the network and data link layers. The distinction between in interface and a layer is crucial.
TCP/IP model does not distinguish between the physical and data link layers.
  Physical layer has to do with the transmission characteristics of the medium used (copper wire, fiber optics, wireless communication, etc.).
  Data link layer job is to delimit the start and end of frames and get them from one side to the other with the desired degree of reliability.
IP and TCP protocols were carefully thought out and well implemented, however, the other protocols were ad-hoc.
  Example - TELNET designed for a ten-character-per second mechanical Teletype terminal and it does not know anything about graphical user interfaces and mice.

## Slide 112: Example Networks
Internet
ARPANET
NSFNET
Third-generation mobile phone networks
Wireless LANs: 802.11
RFID and sensor networks

## Slide 113: Internet
Is a vast collection different networks that use certain common protocols and provide certain common services.

## Slide 114: The ARPANET
Structure of the telephone system.
Baran’s proposed distributed switching system.

## Slide 115: The ARPANET (2)
The original ARPANET design

## Slide 116: The ARPANET (3)
Growth of the ARPANET.
December 1969.
July 1970.
March 1971.

## Slide 117: The ARPANET (4)
Growth of the ARPANET.
April 1972.
September 1972.

## Slide 118: NSFNET
The NSFNET backbone in 1988.

## Slide 119: Architecture of the Internet
Overview of the Internet architecture

## Slide 120: Third-Generation Mobile Phone Networks (1)
Cellular design of mobile phone networks

## Slide 121: Third-Generation Mobile Phone Networks (2)
Architecture of the UMTS 3G mobile phone network.

## Slide 122: Third-Generation Mobile Phone Networks (3)
Mobile phone handover (a) before, (b) after.

## Slide 123: Wireless LANs: 802.11 (1)
Wireless network with an access point.
Ad hoc network.

## Slide 124: Wireless LANs: 802.11 (2)
Multipath fading

## Slide 125: Wireless LANs: 802.11 (3)
The range of a single radio may not cover the entire system.

## Slide 126: RFID and Sensor Networks (1)
RFID used to network everyday objects.

## Slide 127: RFID and Sensor Networks (2)
Multihop topology of a sensor network

## Slide 128: Network Standardization
Who’s Who in telecommunications
Who’s Who in international standards
Who’s Who in internet standards

## Slide 129: Who’s Who in International Standards (1)
The 802 working groups. The important ones are marked with *.
The ones marked with  are hibernating. The one marked with † gave up and disbanded itself.

## Slide 130: Who’s Who in International Standards (2)
The 802 working groups. The important ones are marked with *.
The ones marked with  are hibernating. The one marked with † gave up and disbanded itself.

## Slide 131: Metric Units (1)
The principal metric prefixes

## Slide 132: Metric Units (2)
The principal metric prefixes

## Slide 133: End
Chapter 1