## Slide 1: The Data Link Layer
Chapter 3

## Slide 2: Data Link Layer Design Issues
Encoding, framing, error detection, reliable delivery, and access mediation
Network layer services
Framing
Error control
Flow control

## Slide 3: Data Link Layer
Algorithms for achieving:
  Reliable, +
  Efficient, communication of a whole units – frames (as opposed to bits – Physical Layer) between two machines.
Two machines are connected by a communication channel that acts conceptually like a wire (e.g., telephone line, coaxial cable, or wireless channel).
Essential property of a channel that makes it “wire-like” connection is that the bits are delivered in exactly the same order in which they are sent.

## Slide 4: Data Link Layer
For ideal channel (no distortion, unlimited bandwidth and no delay) the job of data link layer would be trivial.
However, limited bandwidth, distortions and delay makes this job very difficult.

## Slide 5: Data Link Layer Design Issues
Physical layer delivers bits of information to and from data link layer. The functions of Data Link Layer are:
  Providing a well-defined service interface to the network layer.
  Dealing with transmission errors.
  Regulating the flow of data so that slow receivers are not swamped by fast senders.
Data Link layer
  Takes the packets from Physical layer, and
  Encapsulates them into frames

## Slide 6: Data Link Layer Design Issues
Each frame has a
  frame header – a field for holding the packet, and
  frame trailer.
Frame Management is what Data Link Layer does.
See figure in the next slide:

## Slide 7: Packets and Frames
Relationship between packets and frames.

## Slide 8: Services Provided to the Network Layer
Principal Service Function of the data link layer is to transfer the data from the network layer on the source machine to the network layer on the destination machine.
  Process in the network layer that hands some bits to the data link layer for transmission.
  Job of data link layer is to transmit the bits to the destination machine so they can be handed over to the network layer there (see figure in the next slide).

## Slide 9: Network Layer Services
(a) Virtual communication. (b) Actual communication.

## Slide 10: Possible Services Offered
Unacknowledged connectionless service.
Acknowledged connectionless service.
Acknowledged connection-oriented service.

## Slide 11: Unacknowledged Connectionless Service
It consists of having the source machine send independent frames to the destination machine without having the destination machine acknowledge them.
Example: Ethernet, Voice over IP, etc. in all the communication channel were real time operation is more important that quality of transmission.

## Slide 12: Acknowledged Connectionless Service
Each frame send by the Data Link layer is acknowledged and the sender knows if a specific frame has been received or lost.
Typically the protocol uses a specific time period that if has passed without getting acknowledgment it will re-send the frame.
This service is useful for commutation when an unreliable channel is being utilized (e.g., 802.11 WiFi).
Network layer does not know frame size of the packets and other restriction of the data link layer. Hence it becomes necessary for data link layer to have some mechanism to optimize the transmission.

## Slide 13: Acknowledged Connection Oriented Service
Source and Destination establish a connection first.
Each frame sent is numbered
  Data link layer guarantees that each frame sent is indeed received.
  It guarantees that each frame is received only once and that all frames are received in the correct order.
Examples:
  Satellite channel communication,
  Long-distance telephone communication, etc.

## Slide 14: Acknowledged Connection Oriented Service
Three distinct phases:
  Connection is established by having both side initialize variables and counters needed to keep track of which frames have been received and which ones have not.
  One or more frames are transmitted.
  Finally, the connection is released – freeing up the variables, buffers, and other resources used to maintain the connection.

## Slide 15: Framing
To provide service to the network layer the data link layer must use the service provided to it by physical layer.
Stream of data bits provided to data link layer is not guaranteed to be without errors.
Errors could be:
  Number of received bits does not match number of transmitted bits (deletion or insertion)
  Bit Value
It is up to data link layer to correct the errors if necessary.

## Slide 16: Framing
Transmission of the data link layer starts with breaking up the bit stream
  into discrete frames
  Computation of a checksum for each frame, and
  Include the checksum into the frame before it is transmitted.
Receiver computes its checksum error for a receiving frame and if it is different from the checksum that is being transmitted will have to deal with the error.
Framing is more difficult than one could think!

## Slide 17: Framing Methods
Byte count.
Flag bytes with byte stuffing.
Flag bits with bit stuffing.
Physical layer coding violations.

## Slide 18: Byte Count Framing Method
It uses a field in the header to specify the number of bytes in the frame.
Once the header information is being received it will be used to determine end of the frame.
See figure in the next slide:
Trouble with this algorithm is that when the count is incorrectly received the destination will get out of synch with transmission.
  Destination may be able to detect that the frame is in error but it does not have a means (in this algorithm) how to correct it.

## Slide 19: Framing (1)
A byte stream. (a) Without errors. (b) With one error.

## Slide 20: Flag Bytes with Byte Staffing Framing Method
This methods gets around the boundary detection of the frame by having each appended by the frame start and frame end special bytes.
If they are the same (beginning and ending byte in the frame) they are called flag byte.
In the next slide figure this byte is shown as FLAG.
If the actual data contains a byte that is identical to the FLAG byte (e.g., picture, data stream, etc.) the convention that can be used is to have escape character inserted just before the “FLAG” character.

## Slide 21: Framing (2)
A frame delimited by flag bytes.
Four examples of byte sequences before and after byte stuffing.

## Slide 22: Flag Bits with Bit Stuffing Framing Method
This methods achieves the same thing as Byte Stuffing method by using Bits (1) instead of Bytes (8 Bits).
It was developed for High-level Data Link Control (HDLC) protocol.
Each frames begins and ends with a special bit patter:
  01111110 or 0x7E <- Flag Byte
  Whenever the sender’s data link layer encounters five consecutive 1s in the data it automatically stuffs a 0 bit into the outgoing bit stream.
  USB uses bit stuffing.

## Slide 23: Framing (3)
Bit stuffing. (a) The original data. (b) The data as they appear on
the line. (c) The data as they are stored in the receiver’s memory after destuffing.

## Slide 24: Framing
Many data link protocols use a combination of presented methods for safety. For example in Ethernet and 802.11 each frame begin with a well-defined pattern called a preamble.
Preamble is typically 72 bits long.
It is then followed by a length fileld.

## Slide 25: Error Control
After solving the marking of the frame with start and end the data link layer has to handle eventual errors in transmission or detection.
  Ensuring that all frames are delivered to the network layer at the destination and in proper order.
Unacknowledged connectionless service: it is OK for the sender to output frames regardless of its reception.
Reliable connection-oriented service: it is NOT OK.

## Slide 26: Error Control
Reliable connection-oriented service usually will provide a sender with some feedback about what is happening at the other end of the line.
  Receiver Sends Back Special Control Frames.
  If the Sender Receives positive Acknowledgment it will know that the frame has arrived safely.
Timer and Frame Sequence Number for the Sender is Necessary to handle the case when there is no response (positive or negative) from the Receiver .

## Slide 27: Flow Control
Important Design issue for the cases when the sender is running on a fast powerful computer and receiver is running on a slow low-end machine.
Two approaches:
  Feedback-based flow control
  Rate-based flow control

## Slide 28: Feedback-based Flow Control
Receiver sends back information to the sender giving it permission to send more data, or
Telling sender how receiver is doing.

## Slide 29: Rate-based Flow Control
Built in mechanism that limits the rate at which sender may transmit data, without the need for feedback from the receiver.

## Slide 30: Error Detection and Correction
Two basic strategies to deal with errors:
  Include enough redundant information to enable the receiver to deduce what the transmitted data must have been. Error correcting codes.
  Include only enough redundancy to allow the receiver to deduce that an error has occurred (but not which error). Error detecting codes.

## Slide 31: Error Detection and Correction
Error codes are examined in Link Layer because this is the first place that we have run up against the problem of reliability transmitting groups of bits.
  Codes are reused because reliability is an overall concern.
  The error correcting code are also seen in the physical layer for noise channels.
  Commonly they are used in link, network and transport layer.

## Slide 32: Error Detection and Correction
Error codes have been developed after long fundamental research conducted in mathematics.
Many protocol standards get codes from the large field in mathematics.

## Slide 33: Error Detection & Correction Code (1)
Hamming codes.
Binary convolutional codes.
Reed-Solomon codes.
Low-Density Parity Check codes.

## Slide 34: Error Detection & Correction Code
All the codes presented in previous slide add redundancy to the information that is being sent.
A frame consists of
  m data bits (message) and
  r redundant bits (check).
Block code - the r check bits are computed solely as function of the m data bits with which they are associated.
Systemic code – the m data bits are send directly along with the check bits.
Linear code – the r check bits are computed as a linear function of the m data bits.

## Slide 35: Error Detection & Correction Code
n – total length of a block (i.e., n = m + r)
(n, m) – code
n – bit codeword containing n bits.
m/n – code rate (range ½ for noisy channel and close to 1 for high-quality channel).

## Slide 36: Error Detection & Correction Code
Example
Transmitted: 10001001
Received: 10110001
XOR operation gives number of bits that are different.
XOR: 00111000
Number of bit positions in which two codewords differ is called Hamming Distance. It shows that two codes are d distance apart, and it will require d errors to convert one into the other.

## Slide 37: Error Detection & Correction Code
All 2m possible data messages are legal, but due to the way the check bits are computers not all 2n possible code words are used.
Only small fraction of 2m/2n=1/2r are possible will be legal codewords.
The error-detecting and error-correcting codes of the block code depend on this Hamming distance.
To reliably detect d error, one would need a distance d+1 code.
To correct d error, one would need a distance 2d+1 code.

## Slide 38: Error Detection & Correction Code
All 2m possible data messages are legal, but due to the way the check bits are computers not all 2n possible code words are used.
Only small fraction of 2m/2n=1/2r are possible will be legal codewords.
The error-detecting and error-correcting codes of the block code depend on this Hamming distance.
To reliably detect d error, one would need a distance d+1 code.
To correct d error, one would need a distance 2d+1 code.

## Slide 39: Error Detection & Correction Code
Example:
4 valid codes:
  0000000000
  0000011111
  1111100000
  1111111111
Minimal Distance of this code is 5 => can correct double errors and it can detect quadruple errors.
0000000111 => single or double – bit error. Hence the receiving end must assume the original transmission was 0000011111.
0000000000 => had triple error that was received as 0000000111 it would be detected in error.

## Slide 40: Error Detection & Correction Code
One cannot perform double errors and at the same time detect quadruple errors.
Error correction requires evaluation of each candidate codeword which may be time consuming search.
Through design this search time can be minimized.
In theory if n = m + r, this requirement becomes:
  (m + r + 1) ≤ 2r

## Slide 41: Hamming Code
Codeword: b1 b2 b3 b4 ….
Check bits: The bits that are powers of 2 (p1, p2, p4, p8, p16, …).
The rest of bits (m3, m5, m6, m7, m9, …) are filled with m data bits.
Example of the Hamming code with m = 7 data bits and r = 4 check bits is given in the next slide.

## Slide 42: The Hamming Code
Consider a message having four data bits (D) which is to be transmitted as a 7-bit codeword by adding three error control bits. This would be called a (7,4) code. The three bits to be added are three EVEN Parity bits (P), where the parity of each is computed on different subsets of the message bits as shown below.
7 | 6 | 5 | 4 | 3 | 2 | 1 | 
D | D | D | P | D | P | P | 7-BIT CODEWORD
D | - | D | - | D | - | P | (EVEN PARITY)
D | D | - | - | D | P | - | (EVEN PARITY)
D | D | D | P | - | - | - | (EVEN PARITY)

## Slide 43: Hamming Code
Why Those Bits? - The three parity bits (1,2,4) are related to the data bits (3,5,6,7) as shown at right. In this diagram, each overlapping circle corresponds to one parity bit and defines the four bits contributing to that parity computation. For example, data bit 3 contributes to parity bits 1 and 2. Each circle (parity bit) encompasses a total of four bits, and each circle must have EVEN parity. Given four data bits, the three parity bits can easily be chosen to ensure this condition.
It can be observed that changing any one bit numbered 1..7 uniquely affects the three parity bits. Changing bit 7 affects all three parity bits, while an error in bit 6 affects only parity bits 2 and 4, and an error in a parity bit affects only that bit. The location of any single bit error is determined directly upon checking the three parity circles.

## Slide 44: Hamming Code

## Slide 45: Hamming Code
For example, the message 1101 would be sent as 1100110, since:
7 | 6 | 5 | 4 | 3 | 2 | 1 | 
1 | 1 | 0 | 0 | 1 | 1 | 0 | 7-BIT CODEWORD
1 | - | 0 | - | 1 | - | 0 | (EVEN PARITY)
1 | 1 | - | - | 1 | 1 | - | (EVEN PARITY)
1 | 1 | 0 | 0 | - | - | - | (EVEN PARITY)

## Slide 46: Hamming Codes
When these seven bits are entered into the parity circles, it can be confirmed that the choice of these three parity bits ensures that the parity within each circle is EVEN, as shown here.

## Slide 47: Hamming Code
It may now be observed that if an error occurs in any of the seven bits, that error will affect different combinations of the three parity bits depending on the bit position.
For example, suppose the above message 1100110 is sent and a single bit error occurs such that the codeword 1110110 is received:
transmitted message received message
1 1 0 0 1 1 0 ------------> 1 1 1 0 1 1 0
BIT: 7 6 5 4 3 2 1 BIT: 7 6 5 4 3 2 1
The above error (in bit 5) can be corrected by examining which of the three parity bits was affected by the bad bit:

## Slide 48: Hamming Code
7 | 6 | 5 | 4 | 3 | 2 | 1 |  |  | 
1 | 1 | 1 | 0 | 1 | 1 | 0 | 7-BIT CODEWORD |  | 
1 | - | 1 | - | 1 | - | 0 | (EVEN PARITY) | NOT! | 1
1 | 1 | - | - | 1 | 1 | - | (EVEN PARITY) | OK! | 0
1 | 1 | 1 | 0 | - | - | - | (EVEN PARITY) | NOT! | 1

## Slide 49: Hamming Code
In fact, the bad parity bits labeled 101 point directly to the bad bit since 101 binary equals 5. Examination of the 'parity circles' confirms that any single bit error could be corrected in this way.
The value of the Hamming code can be summarized:
Detection of 2 bit errors (assuming no correction is attempted);
Correction of single bit errors;
Cost of 3 bits added to a 4-bit message.
The ability to correct single bit errors comes at a cost which is less than sending the entire message twice. (Recall that simply sending a message twice accomplishes no error correction.)

## Slide 50: Error Detection Codes (2)
Example of an (11, 7) Hamming code correcting a single-bit error.

## Slide 51: Convolutional Codes
Not a block code
There is no natural message size or encoding boundary as in a block code.
The output depends on the current and previous input bits. Encoder has memory.
The number of previous bits on which the output depends is called the constraint length of the code.
They are deployed as part of the
  GSM mobile phone system
  Satellite Communications, and
  802.11 (see example in the previous slide).

## Slide 52: Error Detection Codes (3)
The NASA binary convolutional code used in 802.11.

## Slide 53: Convolutional Encoders
Like any error-correcting code, a convolutional code works by adding some structured redundant information to the user's data and then correcting errors using this information.
A convolutional encoder is a linear system.
A binary convolutional encoder can be represented as a shift register. The outputs of the encoder are modulo 2 sums of the values in the certain register's cells. The input to the encoder is either the unencoded sequence (for non-recursive codes) or the unencoded sequence added with the values of some register's cells (for recursive codes).
Convolutional codes can be systematic and non-systematic. Systematic codes are those where an unencoded sequence is a part of the output sequence. Systematic codes are almost always recursive, conversely, non-recursive codes are almost always non-systematic.

## Slide 54: Convolutional Encoders
A combination of register's cells that forms one of the output streams (or that is added with the input stream for recursive codes) is defined by a polynomial. Let m be the maximum degree of the polynomials constituting a code, then K=m+1 is a constraint length of the code.
Figure 1. A standard NASA convolutional encoder with polynomials (171,133).

## Slide 55: Convolutional Encoders
For example, for the decoder on the Figure 1, the polynomials are:
g1(z)=1+z+z2+z3+z6
g2(z)=1+z2+z3+z5+z6
A code rate is an inverse number of output polynomials.
For the sake of clarity, in this article we will restrict ourselves to the codes with rate R=1/2. Decoding procedure for other codes is similar.
Encoder polynomials are usually denoted in the octal notation. For the above example, these designations are “1111001” = 171 and “1011011” = 133.
The constraint length of this code is 7.
An example of a recursive convolutional encoder is on the Figure 2.

## Slide 56: Example of the Convolutional Encoder
Figure 2. A recursive convolutional encoder.

## Slide 57: Trellis Diagram
A convolutional encoder is often seen as a finite state machine. Each state corresponds to some value of the encoder's register. Given the input bit value, from a certain state the encoder can move to two other states. These state transitions constitute a diagram which is called a trellis diagram.
A trellis diagram for the code on the Figure 2 is depicted on the Figure 3. A solid line corresponds to input 0, a dotted line – to input 1 (note that encoder states are designated in such a way that the rightmost bit is the newest one).
Each path on the trellis diagram corresponds to a valid sequence from the encoder's output. Conversely, any valid sequence from the encoder's output can be represented as a path on the trellis diagram. One of the possible paths is denoted as red (as an example).

## Slide 58: Trellis Diagram
Figure 3. A trellis diagram corresponding to the encoder on the Figure 2.

## Slide 59: Trellis Diagram
Note that each state transition on the diagram corresponds to a pair of output bits. There are only two allowed transitions for every state, so there are two allowed pairs of output bits, and the two other pairs are forbidden. If an error occurs, it is very likely that the receiver will get a set of forbidden pairs, which don't constitute a path on the trellis diagram. So, the task of the decoder is to find a path on the trellis diagram which is the closest match to the received sequence.

## Slide 60: Trellis Diagram
Let's define a free distance df as a minimal Hamming distance between two different allowed binary sequences (a Hamming distance is defined as a number of differing bits).
A free distance is an important property of the convolutional code. It influences a number of closely located errors the decoder is able to correct.

## Slide 61: Viterbi Algorithm
Viterbi algorithm reconstructs the maximum-likelihood path for a given input sequence.

## Slide 62: Error-Detecting Codes (1)
Linear, systematic block codes
Parity.
Checksums.
Cyclic Redundancy Checks (CRCs).

## Slide 63: Parity Bit Error Detection
Block Size (m) 1000 bits from the equation: we need (r) 10 check bits (1011 < 1024).
1 Mbit of data would require 10 kbits.
To detect a block with a single bit of error, one parity bit would suffice.
Once every 1000 blocks (bit error rate is 10-6) one extra block would have to be re-transmitted.

## Slide 64: Parity Bit Error Detection
Problem with multiple bit errors in burst errors.
Considerer the data stream as a matrix of n bits by k bits. Each (k) row is computed a parity.
Interleaving is used to compute parity in different order from that that is being transmitted.
  Compute parity for each n columns
  Transmit the data as k rows.
  The last row we will send the n parity bits.
Example in the next slide gives the case for n=7 and k=7.

## Slide 65: Parity Error-Detecting Codes (2)
Interleaving of parity bits to detect a burst error.

## Slide 66: Parity Error-Detecting Codes
A burst of length n+1 will pass undetected.
The probability of that any of the n columns will have the correct parity by accident is 0.5; the probability of a bad block being accepted as a good one is 2-n.

## Slide 67: Checksum Error-Detecting Codes
A group of parity bits is one example of a checksum.
Stronger checksums are based on a running sum of the data bits of the message.
The checksum is usually placed at the end of the message – complementary sum.
  Errors can be detected by summing the entire received codeword, both data bits and checksum bits.
  If result is zero – no error has been detected.

## Slide 68: Checksum Error-Detecting Codes
Example if checksum is the 16-bit Internet error detection used as part of the IP protocol.
It is applied to 16-bit words.
It will detect an error for cases where parity detection fails.
Checksum error would fail for:
  Deletion or addition of zero data,
  Swapping part of the message,
  Messages splices in which parts of two packets are put together.
Those are typical errors caused by faulty hardware.

## Slide 69: Checksum Error-Detecting Codes
Fletcher’s checksum
  Includes positional component- adding the product of the data and its position to the running sum.
The stronger kind of error-detecting code is Cyclic Redundancy Check (CRC) know as polynomial code.
A k-bit frame is regarded as the coefficient list for a polynomial with k terms ranging from xk-1 to x0

## Slide 70: CRC Error-Detecting Codes
Example:
  110001: 1x5 + 1x4 + 0x3 + 0x2 + 0x1 + 1x0
Module 2 arithmetic –
  Addition and Subtraction are equivalent to exclusive OR.
  Long division is carried the same way except that subtraction operation is again done module 2.

## Slide 71: CRC Error-Detecting Codes
Protocol requires that sender to agree in advance with the receiver on the generator polynomial, G(x).
  Both high- and low-order bits must be 1.
  CRC is computed for a frame of length m- bits corresponding that is longer than the G(x).
  When the receiver gets a checksummed frame it divides it by G(x). If there the result is not equal to zero it means that there has been transmission error.

## Slide 72: CRC Error-Detecting Codes
Algorithm:
  Let r be the degree of G(x). Append r zero bits to the low-order end of the frame so it now contains m+r bits and corresponds to the polynomial xrM(x)
  Divide the bit string corresponding to G(x) into the bit string corresponding to xrM(x) using modulo 2 division.
  Subtract the remanider (which is always r or fewer bits) from the bit string corresponding to xrM(x) using module 2 subtraction. The result is the checksummed frame, T(x), to be transmitted.

## Slide 73: CRC Error-Detecting Codes
Example:
  Frame: 1101011111
  Generator: x4+x+1

## Slide 74: Error-Detecting Codes (3)
Example calculation of the CRC

## Slide 75: CRC Error-Detecting Codes
Certain polynomials have become international standards: IEEE 802
x32 + x26 + x23 + x22 + x16 + x12 + x11 + x10 + x8 + x7 + x4 + x2 + x1 + 1

## Slide 76: Elementary Data Link Protocols (1)
Utopian Simplex Protocol
Simplex Stop-and-Wait Protocol
  Error-Free Channel
Simplex Stop-and-Wait Protocol
  Noisy Channel

## Slide 77: Elementary Data Link Protocols (2)
Implementation of the physical, data link, and network layers.

## Slide 78: Elementary Data Link Protocols
Assumptions:
  A wants to send a long stream of data to machine B.
  It uses reliable connection-oriented service.
  It assumes to have infinite supply of data ready to send,
  It does not have to wait for data to be produced.
  Machines A and B do not crash
  Data link layer treads the data as packets of pure data whose every bit is to be delivered to the destination's network layer.

## Slide 79: Elementary Data Link Protocols
Data Link layer job is to:
  FRAMEING: encapsulate the data packets in a frame by adding the header and trailer.

## Slide 80: Elementary Data Link Protocols
  Error Correction and Detection:
    Control information is added to header, and
    Checksum is added to trailer.
  Frame is then transmitted to the other machine.

## Slide 81: Elementary Data Link Protocols
Library procedures:
  to_physical_layer
  from_physical_layer
  wait_for_event(&event)
    event object will contain the information what has happened.
  In the receiving end:
    Data is being received and the checksum is being computed.
    If the error has occurred the data link layer is being informed: event = chksum_err
    If the data has arrived undamaged: event = frame_arrival.

## Slide 82: Elementary Data Link Protocols (3)
Some definitions needed in the protocols to follow. These definitions are located in the file protocol.h.
. . .

## Slide 83: Elementary Data Link Protocols (4)
Some definitions needed in the protocols to follow. These definitions are located in the file protocol.h.
. . .

## Slide 84: Elementary Data Link Protocols (5)
Some definitions needed in the protocols to follow. These definitions are located in the file protocol.h.

## Slide 85: Utopian Simplex Protocol (1)
A utopian simplex protocol.
. . .

## Slide 86: Utopian Simplex Protocol (2)
A utopian simplex protocol.

## Slide 87: Utopian Simplex Protocol
Unrealistic
  It does not handle flow control
  It does not handle error correction
  Resembles connectionless service that relies on higher layer to solve those problems.

## Slide 88: Simplex Stop-and-Wait Protocol for a Noisy Channel (1)
A simplex stop-and-wait protocol.
. . .

## Slide 89: Simplex Stop-and-Wait Protocol for a Noisy Channel (2)
A simplex stop-and-wait protocol.

## Slide 90: Simplex Protocol
Solves the problem of flow control.
  Blocking acknowledgment of the reception of the frame partially achieves this.
  If acknowledgment frame gets lost the protocol will fail.
  Error correction is not implemented.
  One direction only.

## Slide 91: Sliding Window Protocols
Full duplex data transmission
  Running two instances of one of the previous protocols,
  Each uses separate data link for simplex data traffic in different directions (“forward” channel and “reverse” channel).
Better idea is to use the same channel in both directions.
  A and B frames are intermixed with acknowledgment frames from A and B.
  Kind field in the header of the incoming frame will be used to tell the difference.

## Slide 92: Sliding Window Protocols
In addition to being able to use duplex communication, the further protocol improvement would be to send the acknowledgment frame together with the new data frame. This provides for a “free ride”.
The technique of delaying the acknowledgment for a bit to be added to the next packet is know as piggybacking.
This technique add another complication.
  If the data frame is available within a short time period (less than msec) it will use piggybacking.
  Otherwise, it will send separate acknowledgment.

## Slide 93: Sliding Window
At any instant of time the sender maintains a set of sequences numbers that correspond to frames that are permitted to be send.
Those frames are said to fall within a sending window.
Receiver also maintains a receiving window that corresponds to the set of frames that it is permitted to accept.

## Slide 94: Sliding Window
The sequence numbers within the sender’s window represent the frames that have been sent or can be sent but are not yet been acknowledged.
Whenever the a new packet arrives from the network layer, it is given the next highest sequence number, and
The upper edge of the window is advanced by one.
When acknowledgement arrives the lower edge is advance by one.
This is how the protocol maintains the list of unacknowledged frames.

## Slide 95: Sliding Window Protocols
A sliding window of size 1, with a 3-bit sequence number. (a) Initially. (b) After the first frame has been sent.

## Slide 96: Sliding Window Protocols
A sliding window of size 1, with a 3-bit sequence number
(c) After the first frame has been received. (d) After the first acknowledgement has been received.

## Slide 97: Sliding Window Protocols (1)
A positive acknowledgement with retransmission protocol.
. . .

## Slide 98: Sliding Window Protocols (2)
A positive acknowledgement with retransmission protocol.
. . .

## Slide 99: Sliding Window Protocols (3)
A positive acknowledgement with retransmission protocol.

## Slide 100: One-Bit Sliding Window Protocol
Window size = 1
Stop-and-wait Sender transmits a frame and waits for its acknowledgment before it sends the next one.
Figure of next slide depicts such a protocol.

## Slide 101: One-Bit Sliding Window Protocol (1)
A 1-bit sliding window protocol.
. . .

## Slide 102: One-Bit Sliding Window Protocol (2)
A 1-bit sliding window protocol.
. . .

## Slide 103: One-Bit Sliding Window Protocol (3)
A 1-bit sliding window protocol.

## Slide 104: One-Bit Sliding Window Protocol (4)
Two scenarios for protocol 4. (a) Normal case. (b) Abnormal
case. The notation is (seq, ack, packet number). An asterisk indicates where a network layer accepts a packet

## Slide 105: Protocol Using Go-Back-N
Up-to-know the protocols depicted so far are based on the assumption that the time required for transmission and reception of the acknowledgment packets is negligible.
If this assumptions is not true then round-trip time can have important implications in the efficiency of the communication and the bandwidth utilization.

## Slide 106: Protocol Using Go-Back-N
Example:
  50 kbps satellite channel
  500 msec round-trip propagation delay.
  Lets use Protocol 4 (previous slides) to send a 1000 bit frames via the satellite.
  t = 0: the sender starts the first frame
  t = 20 msec: the frame has been completely sent.
  t = 270 msec: the frame has fully arrived at the satellite.
  t = 520 msec: the acknowledgment has arrived at the sender.
  Sender was blocked 500/520 or 96% of the time. In order to send the packed the sender utilized 4% of the available bandwidth.

## Slide 107: Protocol Using Go-Back-N
The problem?
  Consequence of the rule that requires a sender to wait for an acknowledgment before sending another frame.
  Relaxing this condition will enable achieving significantly better throughput.
Solution!
  Allowing sender the transmit w frames before blocking.
  Acknowledgment will arrive for previous frames before the window becomes full.

## Slide 108: Protocol Using Go-Back-N
Must correctly establish what is the actual size of w.
  Number of frames to fit inside the channel.
  Capacity of the channel is determined by
    Bandwidth in bits/sec
    One-way transit time, or
    The bandwidth-delay product of the link: BD
  The actual size should be set to:
    w = 2BD+1

## Slide 109: Protocol Using Go-Back-N
Example:
  Link with the bandwidth of 50 kbps
  One way transit time of 250 msec
  Bandwidth delay product is BD = 50 kbps x 250 msec = 12.5 kbits or 12.5 frames of 1000 bits.
  2BD+1 = 26 frames.
  t = 0: sends a first frame and subsequent frames after 20 msec.
  t = 520 msec: acknowledgment for the first frame is received, while 26 frames were transmitted.
  Thereafter, acknowledgments will arrive every 20 msec.

## Slide 110: Protocol Using Go-Back-N
  Just in time for the sender to continue transmitting.
  25 or 26 unacknowledged frames will always be outstanding.
  Hence, the senders maximum window size is 26 frames.
For smaller window size, the utilization of the link will be less than 100%.
Upper bound of the link utilization:
  It does not allow for any frame processing time
  Treats acknowledgment frame as having zero length.

## Slide 111: Protocol Using Go-Back-N
From the equation:
  Large bandwidth-delay product requires a large window.
  With stop-and-wait for which w = 1, of there is even one frame’s worth of propagation delay, the efficiency will be less than 50%.
Pipelining – technique where the number of frames (much greater than 1) are send immediately.
What will happen then when a certain frame is received in error?!

## Slide 112: Protocol Using Go-Back-N (1)
Pipelining and error recovery. Effect of an error when
(a) receiver’s window size is 1

## Slide 113: Protocol Using Go-Back-N (2)
Pipelining and error recovery. Effect of an error when
(b) receiver’s window size is large.

## Slide 114: Protocol Using Go-Back-N (3)
A sliding window protocol using go-back-n.
. . .

## Slide 115: Protocol Using Go-Back-N (4)
A sliding window protocol using go-back-n.
. . .

## Slide 116: Protocol Using Go-Back-N (5)
A sliding window protocol using go-back-n.
. . .

## Slide 117: Protocol Using Go-Back-N (6)
A sliding window protocol using go-back-n.
. . .

## Slide 118: Protocol Using Go-Back-N (7)
A sliding window protocol using go-back-n.
. . .

## Slide 119: Protocol Using Go-Back-N (8)
A sliding window protocol using go-back-n.
. . .

## Slide 120: Protocol Using Go-Back-N (9)
A sliding window protocol using go-back-n.

## Slide 121: Cumulative Acknowledgment
When an acknowledgment comes in for frame n, frames n-1, n-2, … are also automatically acknowledged.
Because protocol 5 has multiple outstanding frames, it logically needs multiple timers, one per outstanding frame.
  Each frame times out independently of all the other ones.
  The pending timeouts from a linked list, with each node of the list containing the
    Number of clock ticks until the timer expires,
    Frame being timed,
    A pointer to the next node

## Slide 122: Protocol Using Go-Back-N (10)
Simulation of multiple timers in software. (a) The queued timeouts (b) The situation after the first timeout has expired.

## Slide 123: Selective Repeat
The go-back-n protocol works well if errors are rare.
If the line is poor it wastes a lot of bandwidth on retransmitting frames.
A Selective Repeat protocol allows the receiver to accept and buffer the frames following a damaged or lost one.

## Slide 124: Selective Repeat
Sender and Receiver maintain a window of outstanding and acceptable sequence numbers, respectively.
Sender:
  Window size starts a 0,
  Grows to some predefined maximum,
Receiver:
  Is always fixed in size
  Equal to the predetermined maximum.

## Slide 125: Selective Repeat
Sender and Receiver maintain a window of outstanding and acceptable sequence numbers, respectively.
Sender:
  Window size starts a 0,
  Grows to some predefined maximum,
Receiver:
  Is always fixed in size
  Equal to the predetermined maximum.
  Has a buffer reserved for each sequence number within its fixed window.
  Associated with it is a bit (arrived) telling whether the buffer is full or empty.

## Slide 126: Selective Repeat
Whenever the frame arrives, the receiver does the following:
  Check the frame sequence number if it does fall within its fixed window,
  If this is the case and the sequence has not been received in previous transmissions it will be stored.
  It does so without regard if the frame contains the next packet expected by the network layer.
  This frame is going to be kept until all the lower-numbered frames have already been delivered to the network layer in the correct order.

## Slide 127: Selective Repeat
Consequential receive introduces further constrains on frame sequence numbers vs. the protocols that accepted frames in order.

## Slide 128: Protocol Using Selective Repeat (4)
A sliding window protocol using selective repeat.
. . .

## Slide 129: Protocol Using Selective Repeat (1)
A sliding window protocol using selective repeat.
. . .

## Slide 130: Protocol Using Selective Repeat (2)
A sliding window protocol using selective repeat.
. . .

## Slide 131: Protocol Using Selective Repeat (3)
A sliding window protocol using selective repeat.
. . .

## Slide 132: Protocol Using Selective Repeat (5)
A sliding window protocol using selective repeat.
. . .

## Slide 133: Protocol Using Selective Repeat (6)
A sliding window protocol using selective repeat.
. . .

## Slide 134: Protocol Using Selective Repeat (7)
A sliding window protocol using selective repeat.
. . .

## Slide 135: Protocol Using Selective Repeat (8)
A sliding window protocol using selective repeat.
. . .

## Slide 136: Protocol Using Selective Repeat (9)
A sliding window protocol using selective repeat.

## Slide 137: Selective Repeat
Example:
  3-bit sequence number,
  7 frames are permitted to be send by transmitter, before it is required to wait (for acknowledgment).
Window size restriction:
  Must be at most half the range of the sequence numbers.
  Window size for protocol 6 is (MAX_SEQ+1)/2.

## Slide 138: Protocol Using Selective Repeat (10)
Initial situation with a window of size7
After 7 frames sent and received but not acknowledged.
Initial situation with a window size of 4.
After 4 frames sent and received but not acknowledged.

## Slide 139: Selective Repeat
If there is a lot of traffic in one direction and no traffic in the other direction, the protocol will block when the sender window reaches its maximum.
Axillary timer is started by start_ack_timer after an in-sequence data frame arrives.
  If no reverse traffic has presented itself for piggybacking before the timer expires, a separate acknowledgement will be send.
  Interrupt due to this timer is called ack_timeout event.

## Slide 140: Example Data Link Protocols
Packet over SONET
ADSL (Asymmetric Digital Subscriber Loop)

## Slide 141: Packet over SONET (1)
Packet over SONET. (a) A protocol stack. (b) Frame relationships

## Slide 142: Packet over SONET (2)
Point-to-Point Protocol (PPP) Features
Separate packets, error detection
Link Control Protocol
Network Control Protocol

## Slide 143: Packet over SONET (3)
The PPP full frame format for unnumbered mode operation

## Slide 144: Packet over SONET (4)
State diagram for bringing a PPP link up and down

## Slide 145: ADSL (Asymmetric Digital Subscriber Loop) (1)
ADSL protocol stacks.

## Slide 146: ADSL (Asymmetric Digital Subscriber Loop) (1)
AAL5 frame carrying PPP data

## Slide 147: End
Chapter 3